## Slide 1: Real-time deep learning techniques for N-MRI image acquisition and improvement
Elective in Artificial Intelligence – AI for Visual Perception in HCI and HRI

## Slide 2: Outline
Introduction
Problems in MRI
K-Space
Motion artefact model
Dataset
Current techniques
Project idea

## Slide 3: Introduction
Magnetic Resonance Imaging (MRI) is a safe medical imaging technique used to form pictures of the anatomy and the physiological processes of the body
MRI scanners use strong magnetic fields, magnetic field gradients and radio waves to generate images of the organs in the body
MRI is widely used in hospitals and clinics for medical diagnosis, staging and follow-up of disease without exposing the body to radiations
Important role in the diagnosis, staging and follow-up of the tumors

## Slide 4: Introduction
NeuroImaging
Cardiac MRI
Musculoskeletal
Liver and Gastrointestinal

## Slide 5: Problems in MRI
Obtaining very clear images is crucial!
The long data acquisition time of MRI causes many difficulties in its clinical and research applications
Patient movement during the acquisition of MRI can cause unwanted image artefacts:
  Rigid motion
  Non-rigid motion
Real-time MRI Real-time MRI refers to the continuous imaging of moving objects in real time.
In many cases may make MRI examinations easier and more comfortable for patients, especially for patients who cannot hold their breathings or who have arhythmia

## Slide 6: K-Space
The type of motion artefacts depends on the amount and timing of patient movement with regards to the k-space scan trajectory.
In MRI physics, k-space is the 2D or 3D Fourier transform of the MR image measured. In practice, k-space often refers to the temporary image space, usually a matrix, in which data from digitized MR signals are stored during data acquisition
When k-space is full the data are mathematically processed to produce a final image

## Slide 7: K-Space
Before generation of the MR signal, k-space is just an array of blank cells awaiting the arrival of data. We can think of it as a box of empty ‘pigeon holes’ waiting to receive pigeons. The goal is to put one pigeon in each hole. As long as the box gets filled, the order is unimportant.

## Slide 8: K-Space
Four common k-space trajectories used in modern MR imaging. At the beginning the Cartesian method was used nearly exclusively, however today all these patterns are frequently encountered

## Slide 9: K-Space
Standard sequential Cartesian filling of k-space
Centric ordering of k-space acquisition
Outward radial ordering of k-space

## Slide 10: Motion artefact model
The type of motion artefacts depends on the amount and timing of patient movement with regards to the k-space scan trajectory
Movement at the k-space centre correspond to low image frequencies and result in ghosting artefacts (where the image is repeated)
Movements toward the edges of the k-space correspond to high image frequencies and result in ringing artefacts
Most commonly observed motion artefacts result in minor blurring due to small movements during k-space acquisition

## Slide 11: Motion artefact model
Generate a random movement model by sampling different probability distribution functions. Rotation between (-10°, 10°) and traslation between (-10mm, 10mm)
De-mean the generated movement transform
Apply each ‘de-meaned’ affine transform to the original artefact-free image volume and resample. Then we compute the 3D Fourier Transform of each resampled image
Reconstruct a composite k-space
Transform the k-space to the image domain to produce final artefacted sample

## Slide 12: Dataset
576 MRI scans of healthy patients
Simulated artefacts:
  Rotations between -10° and 10°
  Traslations between -10 mm and 10 mm

## Slide 13: Current Techniques
Modified HighRes3dNet architecture
HR3DNetGAN
[2] - Ben A. Duffy, Wenlu Zhang, Haoteng Tang, Lu Zhao, Meng Law, Arthur W. Toga, Hosung Kim. ‘Retrospective correction of motion artifact affected structural MRI images using deep learning of simulated motion’

## Slide 14: Current Techniques
Metrics obtained comparing ground truth and output image of CNN:
  With simulated corrupted data:
  SSIM (Structural similarity index)
  CC (Pearson correlation coefficient)
  RMSE (Root-mean square error)
  With real corrupted data:
  TCT (Tissue contrast t-score)
[2] - Ben A. Duffy, Wenlu Zhang, Haoteng Tang, Lu Zhao, Meng Law, Arthur W. Toga, Hosung Kim. ‘Retrospective correction of motion artifact affected structural MRI images using deep learning of simulated motion’

## Slide 15: Current Techniques
Pattern related to simulated motion are well corrected
Tissue contrast and sharpness of tissue borders similar to ground truth
Higher values in the metrics with the CNNs models
[2] - Ben A. Duffy, Wenlu Zhang, Haoteng Tang, Lu Zhao, Meng Law, Arthur W. Toga, Hosung Kim. ‘Retrospective correction of motion artifact affected structural MRI images using deep learning of simulated motion’

## Slide 16: Current Techniques
HR3DNet was able to eliminate a large portion of ghosting artifact preserving the sharp tissue boundaries and improving the gray matter-white matter contrast
HR3DNetGAN produces sharper tissue contrast boundaries however it tended to over-enhance edges and regions with residual artifacts
[2] - Ben A. Duffy, Wenlu Zhang, Haoteng Tang, Lu Zhao, Meng Law, Arthur W. Toga, Hosung Kim. ‘Retrospective correction of motion artifact affected structural MRI images using deep learning of simulated motion’

## Slide 17: Current Techniques
U-Net like architecture
The encoder learns to compress relevant information from corrupted MRI discarding the corruption such that decoder is able to restore a clean counterpart
Skip connections from encoder to decoder blocks
Residual connections inside each block from the first layer to the last layer
[3] – Muhammad Usman, Muhammad Umar Farooq, Siddique Latif, Muhammad Asim, Junaid Qadir. ‘Motion Corrected Multishot MRI Reconstruction Using Generative Networks with Sensitivity Encoding’, arXiv:1902.07430v6 [cs.CV], 12 Mar 2020

## Slide 18: Current Techniques
[3] – Muhammad Usman, Muhammad Umar Farooq, Siddique Latif, Muhammad Asim, Junaid Qadir. ‘Motion Corrected Multishot MRI Reconstruction Using Generative Networks with Sensitivity Encoding’, arXiv:1902.07430v6 [cs.CV], 12 Mar 2020
Results obtained for varying degrees of rotational motion:
  Excellecent performances for small amount of motion
  Decay of performance with higher amount of motion

## Slide 19: Project idea
  Develop a DL model capable to solve the correction of corrupted MRI scans ‘offline’
  Optimize and compress the model to make it run on an FPGA accelerator
  Measure the performance of the model on an FPGA accelerator to evaluate its efficiency

## Slide 20: Thanks for your attention

## Slide 21: References
[1] – Richard Shaw, Carole Sudre, Sebastien Ourselin, M. Jorge Cardoso. ‘MRI k-Space Motion Artifact Augementation: Model Robustness and Task-Specific Uncertainty’, Procedings of Machine Learning Research 102:427-436, 2019
[2] - Ben A. Duffy, Wenlu Zhang, Haoteng Tang, Lu Zhao, Meng Law, Arthur W. Toga, Hosung Kim. ‘Retrospective correction of motion artifact affected structural MRI images using deep learning of simulated motion’
[3] – Muhammad Usman, Muhammad Umar Farooq, Siddique Latif, Muhammad Asim, Junaid Qadir. ‘Motion Corrected Multishot MRI Reconstruction Using Generative Networks with Sensitivity Encoding’, arXiv:1902.07430v6 [cs.CV], 12 Mar 2020